QUOTATION SLICING MACHINE GQP-3

GQP-3 Almond Slicing Machine

Main Technical Data

| Model | Capacity | Power | Rev(r/m) | air pressure | Thickness of slice | Outside dimension | Price/FOB Qingdao |
| --- | --- | --- | --- | --- | --- | --- | --- |
| GQP-3 | 50-200kg/h | 1.5kw | 100-700 | 0.3-0.4MPA | 0.3-2mm | 900*550*1500mm | USD3850.00 |
| Noted: The price includes matched electric motor 380V, 50HZ, 3 Phase |

Slicer nuts for peanuts, almonds, cashew nut, walnuts and other nuts slice special equipment.

The machine is equipped with pneumatic feeding device and the slicing apparatus. The nuts into the trough by means of pneumatic nuts pressed into the cutter, cut out the sheet nuts, slicing thickness can be adjusted.

Using high-quality high-speed steel grinding blade, sharp blade, long service life.

Body cover plate made of stainless steel, in line with food hygiene requirements.

ALIDITY OF THE QUOTATION:

This quotation is valid for 2 month only, since we get news that the price of steel will increase recently. So we can update the price 2 month later.

PAYMENTS:

100% prepayment by T/T.

WARRANTEE:

12 MONTH from the date of commissioning, against any manufacturing defects. The guarantee does not include for the wear & tear parts, electrical and faults resulting in any accident/repairs unknown/unauthorized by us.

DELIVERY:

15-20 days from the date of receipt of the confirmed order along with prepayment.